Radio Sounding in the Magnetosphere and Topside Ionosphere

.

BW Reinisch1, DM Haines1, RF Benson2, K Bibl1, G Cheney1, SF Fung2, IA Galkin1,

JM Grebowsky2, JL Green2, X Huang1, R Manning3, and WWL Taylor4

University of Massachusetts Lowell, Center for Atmospheric Research, Lowell, MA

Goddard Space Flight Center, NASA, Greenbelt, MD

Observatoire Paris-Meudon

Raytheon STX, GSFC, Greenbelt, MD

Abstract. Two space borne instruments are being developed to remotely sense plasma distributions in the magnetosphere and the topside ionosphere. The first instrument is the Radio Plasma Imager (RPI); a low frequency sounder designed to sweep from 3 kHz to 3 MHz, which will be part of NASAÕs IMAGE mission to be launched in January 2000. While in the magnetospheric cavity (7 RE altitude), RPI will receive echoes from the magnetopause and the plasmasphere and will measure the direct response of the magnetosphereÕs configuration to changes in the solar wind. With three orthogonal dipole antennas, the angle of arrival of returning echoes will be determined with high accuracy. Similar to modern groundbased ionosondes, RPI will operate like a low-frequency radar system measuring range, location, plasma density, and motion of the reflecting plasma structures.

The second instrument is the TOPside Automated Doppler Sounder (TOPADS) which is being developed for the Ukrainian WARNING mission scheduled for launch in 2001. At a high inclination circular orbit, TOPADS will measure the topside vertical electron density profiles every 75-km along its orbit. Three orthogonal 20 m tip-to-tip dipole antennas will be used for reception, one of them for transmission. Operating as a high-frequency radar, TOPADS will for the first time provide topside plasma velocities by remotely tracking the motions of plasma irregularities. Automatic processing of the ionogram data will provide real time electron density profiles that will be made freely available in real-time as a space weather diagnostics tool.

1   Introduction

For the first time, modern sounding techniques will be applied to the remote sensing of plasma structures above the peak of the F2 layer. The Radio Plasma Imager (RPI) will be flying on NASAÕs magnetospheric Explorer, the IMAGE satellite, to be launched in January 2000, and the Topside Automated Doppler Sounder (TOPADS) is being developed for the Ukrainian WARNING mission. Radio sounding is a well-established technique that was first deployed in the 1920Õs for ionospheric sounding from the ground (Breit and Tuve, 1926). In recent years, advanced digital sounders were developed for groundbased observations that provide detailed information on the structure and dynamics of the bottomside ionosphere (Reinisch, 1996). Radio sounding relies on total reflection of radio waves from plasma structures that have plasma frequencies fN equal to the radio frequencies f. It is, therefore, not possible on the ground to receive echoes reflected from the topside ionosphere or the magnetosphere (i.e., from plasma less dense than the F-layer peak). Topside ionospheric sounders, first developed by Franklin and Maclean (1969), recorded the amplitudes and echo delay times of ionospheric echoes as function of frequency in the same way it was done by the groundbased sounders of the time. Data from the highly successful Alouette/ISIS topside sounders (Jackson et al., 1980; Jackson, 1986) were the basis for nearly 1,000 scientific publications (Benson et al., 1998) The typical frequency range of these analog sounders was 0.1 to 20 MHz corresponding to the plasma frequencies in the ionosphere (Pulinets, 1989). For magnetospheric sounding the required frequency range is 3 kHz to 3 MHz, corresponding to electron densities Ne ( 105 to 1011 m-3, since

The potential use of IMAGE data for space weather analysis and forecasting is summarized in Table 1.

| Imager | Data Product (Level-1) | Derived Quantities |
| --- | --- | --- |
| RPI |

Plasmagram

Echo Map

f(t) Spectogram (1/orbit)

Distance to Magnetopause, Plasmapause,

Polar Cusp (when observed)

Magnetospheric shape (with model), structure,

Gross irregularities

Storm conditions from a plasma/radio wave Perspective

SI

FUV auroral image at (121.6 nm)

FUV auroral image (135.6 nm)

Structure and intensity of the Proton Aurora

| Structure and intensity of the Electron Aurora |
| --- |
| WIC | Aurora Image (140-190 nm) |

Size and shape of Auroral Oval from intensities

| Of LBH bands |
| --- |
| GEO | Lyman alpha image (121.6 nm) | Integrated line-of-sight density map of the EarthÕs geocorona |
| EUV | Plasmasphere He+ image (30.4 nm) | Plasmaspheric density structure and plasmaspheric processes |

HENA

MENA

Neutral atom image (10-500 keV)

Neutral atom image (1-30 keV)

Neutral atom image of composition and energy of the Ring Current and near-Earth Plasma Sheet

Both instrument data combined to make a provisional Dst index

| Plasma Sheet and Ring Current injection dynamics, structure, shape and local time extent |
| --- |
| LENA | Neutral Atom Image (10-500 eV) |

Neutral atom composition and energy of the Auroral/Cleft ion fountain

Ionospheric outflow

Table 1. IMAGE space weather measurements

2   The Radio Plasma Imager on the IMAGE Mission

NASAÕs IMAGE mission is scheduled for launch from Vandenberg, CA, in January 2000. The 13.5 hour orbit will be highly elliptical (Figure 1) with 7 RE altitude at apogee and 1,000 km at perigee. The scientific objective of the mission is to determine the dynamic characteristics of the magnetosphere in response to changes in the solar wind. Remote sensing from a single satellite using imaging techniques can capture the changing characteristics of the magnetospheric plasma structures, from the magnetopause to the auroral ionosphere. IMAGE, which will be NASAÕs first Medium-class Explorer (MIDEX) mission, will carry three different types of sensors: neutral atom imagers, UV imagers, and the radio plasma imager; J. L. Burch of Southwest Research Institute in San Antonio, TX, is the principal investigator of the IMAGE mission. The list of instruments and the instrument lead investigators is shown in Table 2. This ensemble of instruments will address the following questions: (1) What are the dominant mechanisms for injecting plasma into the magnetosphere on substorms and magnetic storm time scales? (2) What is the directly driven response of the magnetosphere to solar wind changes? (3) How and where are magnetospheric plasmas energized, transported, and subsequently lost during storms and substorms? The cartoon in Figure 2 illustrates the Òfield of viewsÓ of the different instruments, and it is immediately evident that RPI ÒseesÓ plasma structures in a different way than do the other instruments. The ÒplasmagramÓ shown on the left side of Figure 2 displays echo delay time versus frequency. RPI employs an active technique: short radio pulses are transmitted into all directions and echoes received from plasma structures with fN = f and gradient vectors parallel to the incident wave normal.

Figure 1. Orbital characteristics of IMAGE

| Image | Measurement | Critical Measurement Requirements | Principal Investigators |
| --- | --- | --- | --- |
| NAI |

Neutral atom composition and energy-resolved images over three energy ranges:

10-500   eV   (LENA)

1-30   keV   (MENA)

10-500 keV (HENA)

FOV: 90¼x90¼ (image ring current at apogee).

Angular Resolution: 8¼x8¼ (LENA), 4¼x8¼ (MENA), 4¼x4¼ (HENA),

Energy Resolution (_E/E): 0.8

Composition: distinguish H and O in magnetospheric and ionospheric sources, interstellar neutrals and solar wind.

Image Time: 4 minutes (resolve sub-storm development).

Sensitivity: effective area 1 cm2 for each sensor.

T.E. Moore, GSFC

D.T. Young, SwRI

| D. Hamilton, Univ. of Maryland |
| --- |
| EUV | 30.4 nm imaging of plasmasphere He+ column densities. |

FOV: 90¼x90¼ (image plasmasphere from apogee),

Spatial Resolution: 0.1 Earth radius from apogee.

Image Time: several minutes to hours resolve plasmaspheric processes).

B.R. Sandel, Univ. of

| Arizona |
| --- |
| FUV | Far ultraviolet imaging of the geocorona at 121.6 nm (GEO) and the aurora at 140-190 nm (WIC) and 121.6 and 135.6 nm (SI) |

FOV: 15¼x15¼ (SI) for aurora (image full Earth from apogee), 1¼x360¼ for geocorona, and 22.4¼x30¼ (WIC)

Spatial Resolution: 70 km (WIC), 90 km (SI)

Spectral Resolution: separate cold geocorona H from hot proton precipitation (_~0.2 nm near 121.6 nm); reject 130.4 nm and select 135.6 nm electron aurora emissions.

| Image Time: 2 minutes (resolve auroral activity). | S.B. Mende, Univ. of California, Berkeley |
| --- | --- |
| RPI |

Remote sensing of electron densities and magnetospheric boundary locations using

Radio sounding.

Density range: 105-1011 m-3 (determine electron density from inner plasmasphere to magnetopause).

Spatial resolution: 500 km (resolve density structures at the magnetopause and plasmapause).

| Image Time: 1 minute (resolve changes in boundary locations. | B.W. Reinisch, Univ. of Massachusetts Lowell |
| --- | --- |

Table 2. IMAGE instruments

Figure 2. IMAGE observations

2.1   Radio Plasma Imaging

2.1.1   The RPI Instrument

The RPI functions as a radar transmitting radio waves simultaneously in all directions and measuring the angle-of-arrival, amplitude, Doppler frequency, and delay times of all echoes (Green et al., 1998). It uses three orthogonal dipole antennas for reception, two of which are 500-m tip-to-tip antennas in the spin plane; these two dipoles are also used for transmission. The third antenna along the spin axis is 20 m long and is used for reception only. Right and left-hand polarized signals can be transmitted by feeding the currents into the long-wire antennas (900 out of phase. This produces a fairly uniform radiation pattern with maxima in the direction of the spin axis and a 3 dB minimum in the spin plane. In a feasibility paper, Calvert et al. (1995) had shown that a 10 W transmitter together with low-noise receivers provide adequate signal to noise ratios to determine range and direction of echo signals up to a distance of at least 4 RE. . Unlike radio sounding on the ground, magnetospheric sounding is not limited by the interference from atmospheric and man-made sources, but by natural external noise, mainly solar noise bursts and storms (Bougeret et al., 1984), auroral kilometric radiation (Gurnett et al, 1979), and the non-thermal (escaping and trapped) continuum (Gurnett, 1975). In comparison, the receiver noise and cosmic noise are usually of less importance but may dominate at certain times and locations. Figure 3 shows a block diagram of RPI, and its specifications are listed in Table 3.

Figure 3.  RPI system configuration

| ITEM | Specifications | Comments |
| --- | --- | --- |

Radiated Power

|  | ( 40 W | (10 W/monopole |
| --- | --- | --- |
| Antennas | 3 orthogonal dipoles |

Two electronically tuned 500m dipoles in spin plane

one 20m dipole along spin axis

Frequencies

|  | 3 kHzÐ3 MHz | 105-1011 m-3 |
| --- | --- | --- |

Bandwidth

|  | 300 Hz | Matched to pulse width |
| --- | --- | --- |
| Pulse Width | 3.2 ms | ( 480 km range resolution |
| Pulse Repetition Rate | 0.5, 1, 2, 4, 10, 20 pps |

Range

|  | 5 RE | SNR depend. |
| --- | --- | --- |

Table 3. RPI specifications

2.1.2   Imaging the Magnetospheric Structures

Electromagnetic wave propagation in a magnetoionic medium is anisotropic and only waves with the so-called characteristic wave polarizations can propagate. The two characteristic polarizations are generally right and left-hand elliptical, and the two characteristic waves propagate with different phase and group velocities, leading to Faraday rotation effects, different plasma cutoff frequencies (reflection levels), and different echo delay times for plasma sounder observations. Since the magnetospheric plasma is inhomogeneous the characteristic polarization slowly changes along the ray path without significant mode conversion, unless steep gradients are encountered, or when f ( fp, where fp is the plasma frequency and f the wave frequency.

RPI uses a quadrature sampling technique to digitize the intermediate frequency available at the receiver output, the same way it is done in the groundbased Digisondes (Bibl and Reinisch, 1978). This makes it easy to adopt the technique of finding the wave normal of the echo signal described by Shawhan (1970). The E field is measured with the three orthogonal antennas at two times separated by a quarter cycle (wt=p/2).  Each 3-antenna measurement determines an instantaneous field vector E(t), and the two quadrature samples give a pair of orthogonal E vectors, Ei = (Ix, Iy, Iz) and Eq = (Qx, Qy, Qz), measured on the x, y, and z antennas. The cross product EixEq determines the orientation of the wave normal n of the arriving wave (Figure 4):

Figure 4. RPI antenna system and the polarization ellipse.

Here it is assumed that that the E field component in the direction of the wave normal is negligible, which is a good approximation as long as fp << f at the satellite location. If the E vector rotates clockwise when looking in the direction of the wave normal, EixEq points in the direction of n, otherwise it points opposite to n. This ambiguity need be resolved with the help of the plasmagram and models of the magneto- and plasmapause. The sense of rotation of the E vector is determined by the direction of the EixEq vector. The accuracy of the angular measurement can be expressed in terms of the voltage signal-to-noise ratio SNR):

For a signal to noise ratio of 100, or 40 dB, the angular accuracy is of the order of 1¡.

2.2   RPI data displays

The distance to the reflection point is approximately given by the virtual range PÕ = _ ctd (c = free space speed of light, td = echo delay time) if fp << f for most of the propagation path between the spacecraft and the reflection point. Accurate target distances can be calculated from the plasmagrams giving PÕ as function of frequency by ÒinvertingÓ the PÕ(f) plasmagram traces. Simulated traces of plasmasphere and magnetopause echoes are shown in Figure 5 for an assumed plasma distribution. The figure shows the Òordinary waveÓ (Budden, 1985) echoes only; the extraordinary echo traces (not shown) only differ slightly. The satellite altitude is assumed as 6 RE where the model plasma frequency is about 3 kHz (Ne = 105 m-3). The maximum frequency reflected from the magnetopause is 41 kHz, corresponding to NE = 1.8x103 m-3. So-called profile inversion programs (Jackson, 1969; Huang and Reinisch, 1982) are available that calculate the Ne(R) profiles from the PÕ(f) traces (X. Huang, personal communication).

It is difficult to present RPIÕs multi-dimensional sounding data in one image, since for each sounding frequency, echoes can arrive from different directions with different delays (ranges). The most direct display is the plasmagram, which is similar to an ionogram, but it does not show the angles-of-arrival. A complimentary image will be the echo-map, a simulation of which is shown in Figure 6. Here the measured reflection points are projected into the orbital plane and a model plasmasphere, magnetopause and cusp is superimposed. The plasma frequency for each reflection point is indicated by the gray shading (color in the planned browse product displays). In this simulation, echoes were received from the plasmasphere/ionosphere, the magnetopause, and the cusp. Uniform gray shading is used for the ÒghostÓ echo locations produced by the 180¡ ambiguity in the arrival angle.

Figure 5.  Ne distribution (dashed curve) as function of altitude (left scale), and the simulated plasmagram (right scale) with echoes from the plasmasphere and magnetopause.

Figure 6. Simulated RPI echo-map with superimposed model of the magnetosphere.

Topside Sounder

A TOPside Automated Doppler Sounder (TOPADS) is being designed for flight on the Ukrainian WARNING mission, tentatively scheduled for launch in 2001. The design concepts for TOPADS are derived from UMLÕs highly successful groundbased ionosonde, the Digisonde Portable Sounder (DPS) (Reinisch et al., 1997). The same imaging technique described for RPI will be used by TOPADS. The frequency range of the topside sounder must be different, of course, to measure ionospheric densities from 108 to 1013 m-3, i. e., 0.5 to 30 MHz. A high inclination circular orbit at 600 to 800 km altitudes is planned. The specifications for TOPADS are summarized in Table 4. Three orthogonal 20-m dipole antennas will be used for reception, and one of them for transmission. The transmit antenna will be electronically tuned to optimize the transmission efficiency. Ten watts of radiated power will produce signal-to-noise ratios of 30 to 40 dB, making use of the digital processing gain obtained by applying the pulse compression and Fourier analysis techniques developed for the DPS. Use of a staggered sequence of 33.3 ms pulses will expand the Doppler frequency range to (1 kHz, large enough to avoid aliasing caused by the satellite motion.

By measuring the angleÐof-arrival and the Doppler shift of the ionospheric echoes it will be possible to determine the vertical electron density in real time, and also to calculate the velocity of ionospheric irregularities. Figure 7 illustrates the different echoes that can be expected at the satellite. By identifying and disregarding the oblique echoes, the vertical echo trace can be automatically scaled and the vertical Ne profile calculated (Reinisch and Huang, 1982; Huang and Reinisch, 1982). The availability of topside profiles will be a valuable input to space weather forecasting. By analyzing the Doppler frequencies for the different echoes it will be possible to determine the drift velocity of the plasma irregularities similar to the method used by the groundbased Digisondes (Cannon et al., 1991; Smith et al., 1998).

| System Parameter | Nominal | Limits | Rationale |
| --- | --- | --- | --- |
| Radiated Power | < 10 W, 5% or 10% duty cycle | 10 W | Produces adequate SNR |
| Frequency Range | 2-18 MHz | 0.5 - 30 MHz | Measure in-situ and F-layer plasma densities |
| Frequency Steps | 2.5% steps | 1 Hz to 500 kHz | Provides 5% in plasma density resolution |
| Time/ionogram or echo-map | 10 s | > 4 s | 75 km along orbit path |
| Maximum Range | 3000 km | 3000 km | vertical and ducted echoes |
| Minimum Range | 40 km | 10 km using short pulses | No reception is possible during transmission |

Range Increments/iono

/echo-map

256 x 2.5 km

| 32 x 20 km | 2.5, 5, 20 km | Sample period = range resolution |
| --- | --- | --- |
| Waveforms |

Compl. phase code

Staggered pulses

| Chirp |
| --- |
| Pulse Rep Rate | 200 Hz or SPS |

50, 100, 200 Hz or

| SPS | Provides required unambiguous range and Doppler range |
| --- | --- |

Pulse Width/iono

/echo-map

33.3 ms

| 266.7 ms | 1 or 8 x 33.3 ms |
| --- | --- |

5 km resolution /

40 km resolution

Rec. Bandwidth/iono

/echo-map

30 kHz

4 kHz

30 kHz

| 4 kHz | Consistent with XTR pulse width |
| --- | --- |

Rec. Sensitivity/iono

/echo-map

500 nV

125 nV

Keeps receiver noise below cosmic noise

Coherent Integr./iono

/echo-map

80 ms

| 10 s | 40 ms - 10 s |
| --- | --- |

Provides processing

gain & Doppler resolution

Doppler Resolution/iono

/echo-map

12 Hz

| 0.1 Hz | 0.1 Hz | Given by coherent integration time |
| --- | --- | --- |

Doppler Range/iono

/echo-map

±1 kHz

| ±100 Hz | ±1 kHz | SPS waveform eliminates Doppler ambiguities |
| --- | --- | --- |
| Rec. Saturation Recovery | 100 ms |
| Specially designed monostatic radar receiver |
| Amplitude Resolution | 3 dB | 3/8 dB | typical display is 3 dB |
| Angle-of-Arrival Res. | 2o | 1o if SNR > 40 dB | Identifies echo direction |

Table 4. TOPADS specifications

Figure 7. Vertical and oblique echoes received by TOPADS.

4.   Summary

Two modern radio sounders are being developed for deployment in the next few years, one for magnetospheric the other for topside sounding. The angle-of-arrival and Doppler measurement capabilities will make it possible to ÒimageÓ the positions of the plasma boundaries and irregularities, and give information about the velocities of the plasma structures.

References

Benson, R.F., Reinisch, B.W., Green J.L., Fung, S.F., Calvert, W., Haines, D.M., Bougeret, J.L., Manning, R., Carpenter, D.L. Gallagher, J.L., Reiff, P. and Taylor, W.W.L., Magnetospheric radio sounding on the IMAGE mission, Radio Science Bulletin, No. 285, ISSN 1024-4530, International Union of Radio Science, URSI, c/o University of Gent, 9-20, 1998.

Bibl, K. and Reinisch, B.W., The universal digital ionosonde, Radio Sci., 13, 519-530, 1978.

Bougeret, J.L., Fainberg, J. and Stone, R.G., Interplanetary radio storms, 1, Extension of solar active regions throughout the interplanetary medium, Astro. Astrophys., 136, 255-262, 1984.

Breit, G. and Tuve, M.A., A test for the existence of the conducting layer, Phys. Rev., 28, 554-575, 1926.

Budden K.G., The propagation of radio waves, the theory of radio waves of low power in the ionosphere and magnetosphere, Cambridge University Press, New York, 669 pp., 1985.

Calvert, W., Benson, R.F., Carpenter, D.L., Fung, S.F., Gallagher, D.L. Green, J.L., Haines, D.M., Reiff, P.H., Reinisch, B.W., Smith, M.F. and Taylor, W.W.L., The feasibility of radio sounding in the magnetosphere, Radio Sci., 30, 1577-1595, 1995.

Cannon, P.S., Reinisch, B.W., Buchau, J. and Bullett, T.W., Response of the Polar Cap F Region Convection Direction to Changes in the Interplanetary Magnetic Field: Digisonde Measurements in Northern Greenland, J. Geophys. Res., 96, A2, 1239-1250, 1991.

Franklin, C.A. and Maclean, M.A., The design of swept-frequency topside sounders, Proc. IEEE, 57, 897-929, 1969.

Green, J.L., Taylor, W.W.L., Fung, S.F., Benson, R.F., Calvert, W., Reinisch, B.W., Gallagher, D. and Reiff, P., Radio Remote Sensing of Magnetospheric Plasmas, Measurement Techniques in Space Plasmas: Fields, 193-198, 1998.

Gurnett, D.A., The Earth as a radio source: The nonthermal continuum, J. Geophys. Res., 80, 2751-2763, 1975.

Gurnett, D.A., Anderson, R.R., Scarf, F.L., Fredricks, R.W. and Smith, E.J., Initial results from the ISEE 1 and 2 plasma wave investigation, Space Sci. Rev., 23, 103-122, 1979.

Huang, X. and Reinisch, B.W., Automatic calculation of electron density profiles from digital ionograms 2. True height inversion of topside ionograms with the profile-fitting method, Radio Sci., 17, 837-844, 1982.

Jackson, J.E., Alouette-ISIS Program Summary, NSSDC Report 86-09, National Space Science Data Center, Greenbelt, MD, 1986.

Jackson, J.E., Schmerling, E.R. and Whitteker, J.H., Mini-review on topside sounding, IEEE Trans. Antennas Propagat., AP-28, 284-288, 1980.

Pulinets, S.A., Prospects of topside sounding, in WITS Handbook No. 2, edited by C.H. Liu, SCOSTEP Publishing, Urbana, IL, 99-127, 1989.

Shawhan, S.D., The use of multiple receivers to measure the wave characteristics of very-low-frequency noise in space, Space Science Reviews, 10, 689-736, 1970.

Smith, P.R., Dyson, P.L., Monselesan, D.P. and Morris, R.J., Ionospheric convection at Casey, a southern polar cap station, J.  Geophys. Res. 103, No. A2, 2209-2218, 1998.

Reinisch, B.W., Modern Ionosondes, in Modern Ionospheric Science, edited by H. Kohl, R. RŸster and K. Schlegel, European Geophysical Society, Katlenburg-Lindau, Germany, 440-458, 1996.

Reinisch, B.W., Haines, D.M., Bibl, K., Galkin, I., Huang, X., Kitrosser, D.F., Sales, G.S. and Scali, J.L., Ionospheric sounding in support of over-the-horizon radar, Radio Sci., 32, 4, 1681-1694, July-August 1997.

Reinisch, B.W. and Huang, X., Automatic Calculation of Electron Density Profiles from Digital Ionograms, 1. Automatic O and X trace identification for topside ionograms, Radio Sci., 17, 421-434, 1982.